## Slide 1
51ˢᵗ Annual Natural Hazards Research and Applications Workshop
June 14-17, 2026 | Broomfield, CO
Community-Powered Power Systems and Why They Work
Dr. John (“Sustainable Jack”) Martin
Lowlander Center
SustainableJack.com
Sky Power for the People, Inc.
Tuesday, June 16, from 3:30 to 5:00 p.m. MDT in Interlocken B

## Slide 2
A modular, portable, battery-powered 2-8 kw solar system that can be transported in a pickup truck or small trailer. It is scalable to multiple units with the size to meet the applications.
Suitable for everyday use, disaster response, and rentals. Rentals can be for homes, businesses, disaster situations, or special events.
A Product
A workshop with design, logistics, maintenance, and training community members. It can be completed in 20 hours or less.
Community members don’t need a massive amount of knowledge to build these units. The workshop is meant for novices with basic skills with hand tools and utilizes community resources. Building the units allows them to understand and service them later.
A Process

## Slide 3
Commercial Portable Units Can Cost $30,000 and up
(~$10 per watt)

## Slide 4
Sky Power for the People

## Slide 7
4.55 kWh Portable Solar · System Inventory & Costs
System components · Prices as of August 2024
Component | Spec | 1-unit qty | 1-unit cost | 3-unit qty | 3-unit cost
Solar panels | Solever 455w (2024) · 10 panels | 10 | $1,865.50 | 30 | $5,596.50
Inverter | EG4 3kW | 1 | $674.00 | 3 | $2,022.30
Batteries | 5 kWh | 1 | $1,495.00 | 3 | $4,305.00
Server rack | HT-W6412 | 1 | $100.00 | 3 | $300.00
Total (excl. racking) |  |  | $4,134.50 |  | $12,223.80
Racking tube inventory
80/20 Ready Tube 9701 · 1.50" × 1.50" square profile predrill · $0.56/in = $6.72/ft · Prices as of August 2024
Tube size | per unit | 1-unit cost | × 3 units | 3-unit cost
3 × 3 ft | 9 |  | 27 | 
5 × 4 ft | 20 |  | 60 | 
3 × 6 ft | 18 |  | 54 | 
13 × 9 ft | 117 |  | 351 | 
3 × 11 ft | 33 |  | 99 | 
Total pieces | 197 |  | 591 | 
Tube cost |  | $1,323.84 |  | $3,971.52
Hardware |  | $200.00 |  | $600.00
Racking total |  | $1,523.84 |  | $4,571.52
Prices as of August 2024 · 5 kWh battery option

## Slide 8
4.55 kWh Portable Solar · Cost Reduction 2024 → 2026
August 2024
June 2026
Chart: 
| Solar Panels | Racking | Batteries | Inverter
Cost | 1865.5 | 1523.84 | 1495 | 674
Chart: 
| Solar Panels | Racking | Batteries | Inverter
Cost | 1628 | 1916 | 251 | 435
$5,559
1 unit
$4,230
1 unit
$1,866
34%
Solar Panels
$1,524
27%
Racking
$1,495
27%
Batteries
$674
12%
Inverter
$1,628
38%
Solar Panels
$1,916
45%
Racking
$251
6%
Batteries
$435
10%
Inverter
The world was
working against it...
30% tax credits — gone
Import tariffs ↑
Additional taxes ↑
Inflation ↑
▼
− 24%
− $1,329
...and it won anyway.
Battery prices have fallen dramatically — 5 kWh option dropped from $1,495 (2024) to $251 (2026)

## Slide 9
Demonstrated portability
(c) 2024 by Sustainable Jack, Dr. John H. Martin.
Built three portable units. Two members have since sponsored their own workshops.
Accomplishments for first workshop

## Slide 10
Proof of Concept
From the Lowlander Center Website. https://www.lowlandercenter.org/news-updates

## Slide 11
Evolving Future:
Designs of Systems and Next Stages of Project
Development

## Slide 12
Upgrade from 10 panels to 8 panels
Upgrade training
Purchase examples of appliances
    air conditioners/heat pumps
    water pumps
    refrigerators
    ice makers and ice houses
    induction stoves
    water purifiers
    waste water aerators
    laundry washers
(c)
Upgrade 2 kWh BOS to 8kw

## Slide 13
    20-foot TEU shipping containers of materials for disaster/emergency training
    Dog & pony show of pickup truck portable unit with trailer of deployed unit and rollout of 10 kWh BOS with 2-4 panels
    Share videos of units
    Power desalination units and aerator units for water purification
    Power skiffs and shanty boats with solar and wind

## Slide 14
Thank You
*Sky Power to the People was first coined by Joe Jordan.
See his TEDx at: https://youtu.be/R1y2wll2Ve8?si=5l224gbk9CKg50gF